## Slide 1
Analysis of Real samples (chem. 422)
DEPARTMENT OF CHEMISTRY

## Slide 2: Part I: Water Analysis
EXPERIMENT 1: Analysis of physical characteristics of water sample
Objective : to determine physical characteristics ( odour , color, pH , temperature, electrical conductivity and total dissolved solid (TDS) of surface water ,ground water , wastewater, drinking water and distilled water .
Theory:
pH- Electrometric Method
pH is a logarithmic scale generally used to expressed the acidic , alkaline or neutral nature of a solution.
In fact , it presents the hydrogen ion concentration or more precisely the H+ ion activity in a given solution.

## Slide 3
Source- pH value is best indication of the presence of acid or alkaline in the water sample. Due to hydrolysis of dissolved salts, the pH value can decrease or increase beyond neutral value i.e 7.0 showing in the presence of acidic or alkali in the solution.
The presence of salts of strong base and weak acids e.g. Na2CO3 increase pH value,
salts of weak base and strong acid e.g. CaCl2 decrease pH level. Thus , a fundamental relationship exists among pH, acidity and alkalinity.

## Slide 4
Temperature
This is one of the most essential parameters to determine in water and wastewater systems.
It has significant impact on the growth and activity of ecological life. On the top of that, it great affects the solubility of essential gases such as oxygen in water.
Source- The temperature of natural water systems depends on many factors:
Weather conditions- i.e atmospheric temperature
The subsequence discharge of cooling water in stream used for dissipation of waste heat in industrial
Removal of forest canopies
Waste flows from irrigation sites

## Slide 5
Water Conductivity
It measure of the ability of an aqueous solution to carry an electrical current. This ability depends on the presence of ions, on their total concentration, mobility and valance and on the temperature measurements.
The International system of units (SI) the reciprocal of the ohm is the Siemens(s) and conductivity is measured in micromhos per centimeter (mhos/cm) or microsiemens per centimeter(s/cm), equivalent units of measure that can be used interchangeably.
Drinking water has conductivity in the range of 0.005 to 0.05 S/m.

## Slide 6
Total dissolved solid (TDS)
It is defined as the quantity of dissolved material in water, and depends mainly on the solubility of rocks and soils the water contacts.
For instance, water that flows through limestone and gypsum dissolves calcium, carbonate, and sulfate, resulting in high levels of total dissolved solids.
TDS: is a measure of the total ions in solution in term of its capacity to transmit current.
A convenient way to measure TDS is to test the conductivity of the sample.

## Slide 7
Conductivity is a measure of the ability of water to pass an electrical current and is affected by the presence of dissolved solids. As the level of TDS rises, the conductivity will also increase.
The TDS of a water sample based on the measured EC can be calculated using the folloing equation :
TDS (mg/l) = 0.5 x EC (dS/m or mmho/cm) or
TDS = 0.5 * 1000 x EC (S/cm)
TDS (mg/l) = 640 x EC (dS/m or mmho/cm) …………….. For water for agriculture and irrigation purpose

## Slide 8
Analytical procedures
pH measurements
Reagents: Buffer solutions
Acetate buffer (pH = 4.62)
Acetic acid , CH3COOH, 1M: measure 16mL 94.5% acetic acid in a 250 mL volumetric flask . Make up the final volume to 250 mL with Double Distilled water (DDW.)
Sodium hydroxide , NaOH , 1M : weight 40g NaOH and transfer to a 1L volumetric flask . Dissolve in DDW and bring the final volume to 1L with DDW. Cool the solution.
Measure 200mL acetic acid in a 1L Volumetric flask. Add 100 mL NaOH solution. Bring the final volume up to the mark with DDW. This is an acetate buffer of 4.62 pH.
b) Phosphate buffer pH 7.0
c) Borate buffer pH 9.0

## Slide 9
After calibrating with acetate (pH = 4.01) , phosphate (pH = 7.00) and borate (pH = 10.00) buffers , rinse the electrode with DDW.
Take the sample in a beaker and bring the temperature of the sample to at room temperature and homogeneity using magnetic stirrer. Place the electrode was placed in the sample in such a way that the bar magnet will not touch the electrode.
Record the reading which will give the pH value of the sample
Calculation
The read-out of the pH meter will give direct pH value of the sample.

## Slide 10
Temperature measurement
Measured the air temperature with a dry thermometer approximately above the sampling point. Thermometer must be shaded from the sun.
Measure the water temperature by dipping the thermometer to the required depth in water or wastewater stream or aeration basis and wait until a constant reading is obtained.
Where direct measurement is not possible , collect 5liter water in sampling bottle . Immediately measure the temperature with thermometer.

## Slide 11
Conductivity and TDS measurements
Dipping the electrode directly to the wastewater will do the TDS measurements and its conductivity.

## Slide 12
Please remember , that above outline is very general. Different pH meters may require slightly different operating procedures.
Collect the water and wastewater samples using appropriate sampling technique, sample container and preservative.
Using pH meter, conductivity Bridge meter calculate temperature, pH , electrical conductivity and TDS for water samples
Having a comparison with ISO/ any international standards and comment on the quality of water/ wastewater.

## Slide 13: To Determine the Turbidity of water
Principal: The method is based on a comparison intensity of light of the scattered by the sample under defined conditions with the intensity of light scattered by a standard reference suspension under the same conditions.
Higher the intensity of scattered light, higher the turbidity.
Formazin polymer is used as the primary standard reference suspension.
The turbidity of a specified suspension is defined as 4000NTU (Nephelometric Transparency Unit).

## Slide 14
Interference: Turbidity can be determined for any water sample that is free of debris and rapidly setting coarse sediment.
Dirty glass wares and the presence of air bubbles give false results.
“True color”, i.e. water color due to dissolved substances that absorbed light, causes measured turbidity to be low.
This effect usually is not significant in treated water.

## Slide 15
The apparatus is based on the nephelometric principal of turbidity measurement.
This instrument meets the design criteria specified by the United States Environmental Protection Agency, method 180.1.

## Slide 16
Procedure:
Respective sample is taken in a clean container up to the mark (approximately 15ml), taking care to hold the sample cell by the top. The cell is capped.
The cell is wipped with a soft, lint free cloth to remove water spots and fingerprints.
A thin film of silicon oil is applied and again wipped with a soft cloth to obtain an even film over the entire surface.
Now press 1 / 0 to on power of instrument.
The sample cell is inserted in the instrument cell compartment so the orientation mark aligns with the raised orientation mark in front of the cell compartment. The lid is closed.

## Slide 17
Range is selected by manual or automatic range selection by pressing the RANGE key. The display will show AUTO RNG when the instrument is in automatic range selection.
Signal Average is selected by select signal average key. The display will show SIG AVG when the instrument is using signal averaging. This knob is used when the sample causes noisy signal i.e. reading changes continuously.
READ key is pressed.
The display will show turbidity in NTU (Nephelometric Transparency Unit), the turbidity is recorded after the removal of lamp signal in the display.
Notes: Reference: 1. Portable Turbidimeter, model 2100 P Instrument and Procedure Mannual). Cat.No. 46500-88. Hach Co., 1991-99,2001.
2. Standard Methods for the examination of Water and Waste water, 20th Edition. 1998. APHA.

## Slide 18
Reference:
1. Portable Turbidimeter, model 2100 P Instrument and Procedure Mannual). Cat.No. 46500-88. Hach Co., 1991-99,2001.

## Slide 19
Experiment 2: ALKALINITY
The alkalinity of water is a quantitative measure of the basic constituents of water and is defined as the capacity of the water to neutralize a strong acid at a designated pH.
The alkalinity of natural waters is mainly due to the presence of salts of carbonates, bi-carbonates and hydroxide of calcium, magnesium, sodium and potassium. The borates, silicates & phosphates also contribute to some extent.
Alkalinity value help in deciding chemical doses in water & waste water treatment processes particularly in coagulation, softening and operational control of anaerobic digestion and suitability of water for irrigation purposes.
Notes: Borate: a salt in which the anion contains both boron and oxygen, as in borax.

## Slide 20
PRINCIPLE
Alkalinity of water sample can be estimated by titration with standard acid using phenolphthalein indicator (pH-8.5) or methyl orange indicator (pH-4.5) or with pH meter (Potentiometric method).
Alkalinity is reported in terms of CaCO3 in mg/l.
In the absence of above indicators, metacresol purple (pH-8.3) and bromocresol green (pH-4.5) can also be used for titration.

## Slide 21
INTERFERENCE
The interferences are primarily due to residual chlorine, turbidity, colour etc.
Residual chlorine can be removed by adding thio-sulphate.
Potentiometric titration is recommended for colored & turbid samples.
METHOD FOR DETERMINATION
There are two methods for determination of alkalinity
Titrimetric Method Using Indicator;
Potentiometer Method/ pH metric titration

## Slide 22
REAGENTS
Standard Sodium Carbonate Solution 0.05 N
Dry approximately 5 gm of Na2CO3 (AR grade) at 250oC for 4 hours and then cool in a desiccators for 20 minutes. Weigh approx. 2.5 gm and note the correct weight (A). Then dissolve this Na2CO3 in 1 litre of distilled water. Prepare fresh solution every week.
Standard Sulphuric or Hydrochloric Acid 0.02 N
Dilute 200 ml of 0.1 N H2SO4 or HCl (prepared from 1N acid) to 1 litre with distilled water. H2SO4 (1N) - Dilute 28 ml of concentrated acid to 1 litre with distilled water. HCl (1N) - Dilute 83 ml of concentrated acid to 1 litre with distilled water.

## Slide 23
Standardization of Acid
Take 40 ml of Na2CO3 solution in a beaker and add 60 ml distilled water. Add acid solution (approx. 0.1N) drop-wise to pH-5 using pH meter. Rinse electrode with distilled water before and after use each time. Boil the mixture for approx. 5 min. covering with a watch glass. Then cool to room temperature, rinse watch glass with distilled water and complete titration to pH inflection point.
Calculation
A x B
Normality (N)= ----------
53 x C
A= Exact weight of Na2CO3 taken for 1 litre of solution
B = ml of Na2CO3 taken for titration
C = ml of Acid used; 1 ml of 0.1 N Acid = 5 mg CaCO3 OR
1 ml of 0.02 N Acid = 1 mg CaCO3

## Slide 24
Phenolphthalein Indicator Solution (pH 8.3)
Dissolve 1 gm phenolphthalein in 100 ml 95% ethyl alcohol or isopropyl alcohol and 100ml distilled water.
Methyl orange Indicator Solution (pH-4.5)
Dissolve 0.5 gm methyl-orange powder in distilled water and dilute to 1 litre with distilled water.
Metacresol Purple Indicator Solution (pH-8.3)
Dissolve 0.1 gm of metacresol purple in 100 ml distilled water.
Bromocresol Green Indicator Solution (pH-4.5)
Dissolve 0.1 gm of bromocresol green sodium salt in 100 ml distilled water.
Sodium Thio-sulphate 0.1 N
Dissolve 24.82 gm Na2S2O35H2O in 1 litre of distilled water.

## Slide 25
PROCEDURE
Titrimetric Method
Take 100 ml sample or an aliquot diluted to 100 ml in a conical flask of 300 ml capacity.
Add 1 ml of 0.1 N Na2CO3 per mg of residual chlorine, if present.
Add 5 drops of phenolphthalein indicator if pink colour appears titrate with 0.02N H2SO4 or HCl to the colorless end point. (pH-8.3). Note down the volume of acid consumed. (A).
Add 5 drops of methyl-orange indicator to the above solution, if yellow colour appears continue titration with acid till pink end point (pH-4.5). Note the volume of acid consumed (B).
Note: If, pink colour does not appear on addition of phenolphthalein indicator phenolphthalein Alkalinity is absent.

## Slide 26
Potentiometer Method
Take 100 ml sample in a beaker.
Put the beaker on a magnetic stirrer below the tip of burette filled with 0.02 N H2SO4 or HCl and dipping the pH electrode in the sample.
Put on magnetic stirrer and pH meter and start adding drop-wise 0.02 N acid up to pH 8.3 (if pH is above 8.3). Note down the volume of acid consumed (A).
Continue titration as above till pH is reached at 4.5 + 0.2 and note down the volume (B).
At inflection point, pH changes suddenly.
Notes: Reference: 1. Portable Turbidimeter, model 2100 P Instrument and Procedure Mannual). Cat.No. 46500-88. Hach Co., 1991-99,2001.
2. Standard Methods for the examination of Water and Waste water, 20th Edition. 1998. APHA.

## Slide 27
CALCULATION
ml standard acid used x 1000
Phenolphthalein Alkalinity = ---------------------------------
in mg/l as CaCO3 Volume
Total ml standard acid used x 1000
Methyl-orange Alkalinity or = ----------------------------------
Total Alkalinity in mg/l as CaCO3 Volume

## Slide 28: EXPERIMENT 3 : Analysis of hardness of water sample
Objective : Tap water contains a number of dissolved substance s such as calcium and magnesium in form of carbonate and chloride ions. Presence of metals ions interfere with the cleansing ability water and cause hardness. In this experiment we will analyze water to find capability of ions that cause water to be “ hard.”

## Slide 29
Hard waters are generally considered to be those waters that require considerable amounts of soap to produce foam and that also produce scale in water pipes, heaters, boilers and other units in which the temperature of water is increased.
The cations react with soaps (sodium or potassium salts of fatty acids) to form precipitates:
2C17H15COONa + M2+ ==== (C17H35COO)2M + 2Na+
Sodium stearate Hardness causing (ppt.)
(Soap) cation
Lather is produced only after sufficient soap has been added to precipitate all the hardness causing ions. At higher concentrations, these ions associate themselves with certain anions (CO32+, SO42+, Cl-, NO3-, SiO32-, etc.) and produce scale.
Determination of hardness by EDTA : the amount of Ca2+ and Mg2+ ions in water can be determined by the method of Complexometric titration s
EDTA is hexadentate ligand (two nitrogen and four acetate oxygen centers)

## Slide 30: Ligands
Hexadentate
  ethylenediaminetetraacetate (EDTA) = (O2CCH2)2N(CH2)2N(CH2CO2)24-
  Example Complexes
    [Ca(EDTA)]-2
    [Mg(EDTA)]-2

## Slide 31: Ligands
EDTA
Donor Atoms
*
*
*
*
*
*

## Slide 32: Ligands
EDTA
C
O
N
H
M

## Slide 33: Ligands
EDTA

## Slide 34
Chelation therapy is used in treatment for heavy metal poisoning.
It uses chelating ligands like EDTA that bind very strongly with toxic elements in complexed form and remove them.
Pb, Hg and Cd are toxic elements.

## Slide 35
M2+ + H2Y2-  MY2- + 2H+
Where Y is the chelating agent which is:
The dissociation of these complexes is governed by the pH of the solution and the complexes with hardness causing divalent ions are stable in alkaline medium (pH range 8-10).
The Indicator used is a complex organic compound [sodium-l- (1-hydroxy-2-napthylazo)-6-nitro-2-naphthol-4-sulphonate], commonly known as Eriochrome Black T.
Mg-In + H2Y2-  MgY2- + Hin2- + 2H+
Wine red (metal bound) goes to sky blue(metal unbound form)….end point

## Slide 36
The concentration of the hardening ions in a water sample is commonly expressed as though the hardness is due to exclusively to CaCO3. the unit for hardness is mg CaCO3/L, which is also ppm CaCO3. Waters are commonly classified based on degree of hardness (Table 1):
Hardness (ppm CaCO3) | Classification
< 15 ppm | Very soft water
15 ppm-50ppm | Soft water
50-100ppm | Medium hard water
100-200ppm | Hard water
> 200 ppm | Very hard water

## Slide 37
PROCEDURE
This experiment is conducted in three parts:
Preparation of standard (0.05 M) Mg 2+ solution:
MgSO4.7H2O (FW= 246.47) can be used as primary standard. 1.232 g of this salt when dissolved in water to make 100 mL solution will give 0.05 M solution .
Standardization of EDTA (disodium salt dihydrate FW = 372.2)
10 mL of standard magnesium sulphate solution will be taken in a conical flask and add 3 mL of buffer solution (NH3/NH4Cl) and 3-5 drops of EBT indictor solution and warm-up the contents in conical flask at 400c using hotplate. Wine red color will be observed. The contents in conical flask will be titrated against EDTA solution until blue color appears. From the end point of titration calculate the exact concentration of EDTA.
Determination of Total hardness
Pipette out 50 mL of tap water into conical flask and titrate against standard EDTA solution, following the same procedure as given in above..repeat the titration

## Slide 38
CALCULATION :
Hardness (in mg/L as CaCO3) = (V× N × 50 ×1000) / (SV)
Where: V = volume of titrant (mL); N = normality of EDTA;
50 = equivalent weight of CaCO3; SV = sample volume (mL)
Hardness (in mg/L as CaCO3) = [M2+ (in mg/L) × 50]/ (E.Wt. of M2+
Where: M2+ = mass of divalent ions (mg/L) and E.Wt. = Equivalent weight of divalent ions (g/mole)
Example: If in a sample, 15 mg/L Ca2+are present (, hardness is given by Hardness (in mg/L as CaCO3) =
[mass of Ca2+ (in mg/L) × 50]/ (E.Wt. of Ca2+
Here, E.Wt. of Ca2+ = (40g/mole)/2=20 g/mole
Hardness due to calcium ions = [15 mg/L × 50]/ (20) = 37.5 mg/L CaCO3

## Slide 39: Questions
Why is the sample buffered to a pH of 10? What problems might you expect at a higher pH or a lower pH?
Why does the procedure specify that the titration take no longer than 5 minutes?

## Slide 40: EXPERIMENT 4: Analysis of chemical oxygen demand (COD) of water
Objective : to determine the chemical oxygen demand (COD) of surface and ground water
Introduction: COD test is used widely to estimate the amount of organic matter in wastewater.
It is a measurement of the oxygen equivalent of the materials present in the wastewater that are subject to oxidation by strong chemical oxidant , in the case dichromate
The reactor digestion method test, the COD procedure is greatly simplified over the dichromate reflux method.

## Slide 41
Small volume of the water sample pipetted into vials containing pre-measured reagents, including catalysts and chloride compensator.
The vials are incubated until digestion is completed and then cooled.
The COD determination is made either with the spectrophotometer or titration.
This is accepted for reporting by US Environmental protection agency (EPA).
Notes: Incubated: in a laboratory or other controlled situation) keep (eggs, bacteria, embryos, etc.) at a suitable temperature so that they develop.
compensator: • act so as to neutralize or correct (a deficiency or abnormality in a physical property or effect): the output voltage rises, compensating for the original fall.

## Slide 42
The test measurement the amount of oxygen required for chemical oxidation of organic matter in the sample to carbon dioxide and water.
The test procedure is to be add a known quantity of standard potassium dichromate solution, sulphuric acid reagent containing silver sulphate.
The mixture is refluxed for 2 hrs by COD reactor.
Most types of organic matter are destroyed in this boiling mixture of chromic and sulphuric acid . Eq 1.
Organic matter + Cr2O72- + H+ CO2 + H2O + 2Cr3+
Notes: Reflux: Chemistry the process of boiling a liquid so that any vapour is liquefied and returned to the stock.

## Slide 43
APPARATUS
Reflux Apparatus: Consisting of a flat bottom, 150 to 250 ml. capacity tubes with ground glass joint and long air condensers.
REAGENTS
Standard Potassium dichromate (0.25 N) :Dissolve 12.259 g. potassium dichromate previously dried at 103oC for 24 hours in distilled water and dilute to 1000 ml. Add about 120 mg sulphamic acid to eliminate NO2-N interference.
Sulphuric Acid reagent : Add 22 g. silver sulphate to 4 kg conc. H2SO4 bottle or 10 g to 1000 ml of H2SO4. Keep overnight for dissolution. Shake well after dissolution.
Standard Ferrous Ammonium Sulphate (0.1 N) :Dissolve 39 of Fe (NH4)2(SO4)2. 6H2O in distilled water. Add 20-ml. conc. H2SO4, cool and dilute to 1 litre. Standardize this solution daily against the standard K2Cr2O7.
Standardization: Dilute 10-ml. standard K2Cr2O7 solution to about 100 ml-distilled water. Add 30 ml. conc. H2SO4 and cool. Add 3-4 drops of ferroin indicator and titrate with ferrous ammonium sulphate till the colour change to wine red.
Normality of ferrous ammonium sulphate = 10 x 0.25/ml of Fe (NH4)2(SO4)2
Ferroin Indicator: Dissolve 1.485 g. 1.10 phenanthroline monohydrate and 605 mg FeSO4-7H2O in water and dilute to 100 ml. This indicator solution could be also purchased already prepared.
Mercuric sulphate
Notes: sulphamic acid |sʌlˈfamɪk|(US sulfamic acid )
noun [ mass noun ] Chemistry
a strongly acid crystalline compound used in cleaning agents and to make weedkiller.
●Chem. formula: HOSO 2NH 2.

## Slide 44
PROCEDURE
Place 0.4g HgSO4 in a reflux tube. Add 20 ml of sample or an aliquot of sample diluted to 20 ml with distilled water. Mix well, so that chlorides are converted into poorly ionized mercuric chloride.
Add 10 ml. standard K2Cr2O7 followed by slowly 30 ml. sulphuric acid which already contains silver sulphate. This slow addition along with swirling prevents loss of volatile materials such as fatty acid, in the sample. Mix well if the colour turns green either takes fresh sample with smaller aliquot or add more dichromate and acid. Final conc. of H2SO4 should be always 50%.
Connect the tube to condenser and reflux for 2 hrs. Cool and wash down the condensers with small quantity of distilled water.
Remove the flask and add about 80 ml distilled water. Cool and titrate against standard ferrous ammonium sulfate using ferroin as indicator. Colour changes sharply from green blue to wine red.
Reflux a reagent blank under identical conditions, preferably simultaneously with the sample.
Notes: Aliquot: a portion of a larger whole, especially a sample taken for chemical analysis or other treatment.

## Slide 45
ALTERNATE PROCEDURE FOR LOW‑COD SAMPLES (BELOW 50 mg/l)
The method is same as for the high ‑ COD samples except in this case the concentrations of K2Cr2O7 and ferrous ammonium sulphate is reduced i.e. K2Cr2O7, 0.05 N and ferrous ammonium sulphate, 0.025 N.
Exercise extreme care with this procedure because even a trace of organic matter in the glassware or the atmosphere may cause a gross error. COD values upto 160 mg/l can be estimated by this procedure.

## Slide 46
CALCULATION
mg/lit. COD = (a‑b) Nx8000
Where: ml. Sample
a - is the ml FAS required for blank
b - is the ml FAS required for sample
N - is the normality of FAS
Notes: FAS - ferrous ammonium sulphate

## Slide 47
PRECAUTIONS
The strength of sulfuric acid in final solution should be 18 N i.e. 50%.
The trend of making mixture should be HgSO4, sample (Swirl), K2Cr2O7 and conc. H2SO4.
As far as possible, reflux blank and samples simultaneously.
After refluxing, cool, use required amount of distilled water for washing the container. Cool and then titrate.
REFERENCE
APHA (American Public Health Association), (1998): Standard Method for Examination of Water and Wastewater (20th Edition), Washington, D.C., USA. P.5.12 -5.14.

## Slide 48
EXPERIMENT 5: Water Analysis for Dissolved oxygen
Objective : Determination of dissolved oxygen (DO) of surface and ground water or wastewater
Theory:
Knowledge of the DO concentration in sea water is often necessary in environmental and marine science.
For the marine chemist it provides a measure of the redox potential of the water column.
The concentration of DO can be readily and accurately measured by the method originally developed by Winkler in 1888.
.

## Slide 49
DO can also be determined by two forms
i) using sensitive electrode
ii) Winkler titration
Most of the time the Winkler technique is often employed for accurate determination of oxygen concentrations in aqueous sample.
Where as the sensitive electrodes particularly useful in polluted water where oxygen concentrations may be quite high

## Slide 50
Dissolved Oxygen (DO) in natural and wastewater depends on the physical, chemical and biological activity in a water body.
The analysis for DO is important in water pollution control and waste treatment process control.
DO as a parameter used:
To assess quality of surface‑water and to keep a check on stream pollution
It is the basis for BOD, which is an important parameter to evaluate pollution potential of wastes.
It is responsible for corrosivity, photosynthetic activity and septicity.
DO is necessary for all aerobic biological wastewater treatment processes.

## Slide 51
The Iodometric test (Winkler's method) is precise and reliable titrimetric procedure for DO analysis.
The test is based on the addition of divalent manganese solution, followed by strong alkali, to the sample in a BOD glass‑stoppered bottle.
DO present, rapidly oxidize an equivalent amount of the dispersed divalent manganous hydroxide of higher oxidation state (brownish orange in colour).

## Slide 52
This brownish‑orange colour indicates presence of oxygen.
In the presence of iodide and on subsequent acidification, higher manganese hydroxide revert to the divalent state, and liberate iodine equivalent to the original dissolved oxygen content of the sample.
The iodine liberated is titrated with a standard solution of sodium thiosulfate using starch as an indictor.

## Slide 53
INTERFERENCE
It is caused by certain oxidizing agents, which liberate iodine from iodides. (Such as ozone, chlorine, ferric compounds, manganese in tri or higher oxidation states, chromate, nitrate, persulfate, peroxides, etc.
by certain reducing agents which may reduce iodine to iodide (such as ferrous compounds, thiosulfate, readily oxidizable organic matter, nitrite etc.).
Some organic compounds hinder the settling of the precipitate and colour of the starch end point. Modifications are included for minimize the effect of interfering materials.
Apparatus
The bottle used should be of good quality having 300 ml. capacity with narrow neck and well fitting ground‑glass stopper. It is convenient to have number on bottles and their stoppers.

## Slide 54
REAGENTS
Sulfate Solution
Dissolve 500 g MnSO4, 480 g MnSO4, 4H2O, and 400 g MnSO4 2H2O or 364 g MnSO4 H2O in distilled water. Filter and dilute to 1 litre. This manganous sulfate solution should not give a colour with starch when added to an acidified solution of potassium iodide.
Alkali‑iodide‑azide reagent
Dissolve 500 g NaOH (or 700 g KOH), and 135 g NaI, (or 150 g KI) in distilled water and dilute to 1 litre. Add 10 g sodium azide, NaN3 dissolved in 40 ml distilled water. Potassium and sodium salts may be used interchangeably. This reagent should not give colour with starch solution when diluted and acidified.
Sulfuric acid conc.
Starch Indicator
Make a smooth paste of 5 g soluble starch in cold water and pour this into 1 litre boiling water with constant stirring. Boil for one minute and allow to cool before use. Use clear supernatant. Preserve with 1.25 g salicylic acid or by adding a few drops of toluene.
Notes: Supernatant: denoting the liquid lying above a solid residue after crystallization, precipitation, centrifugation, or other process.

## Slide 55
Sodium Thiosulfate Stock Solution 0.125 N
Dissolve 31.5 g sodium thiosulfate, pentahydrate, Na2S2O3, 5H2O in 1 litre copper free, boiled and cooled distilled water. Add 5 ml chloroform or 1 g NaOH as preservative.
Potassium Iodide, 0.0125 N
Dissolve 0.446 Potassium iodide previously dried at about 120oC, in distilled water and dilute to 1 litre. The solution is table for a long period if stored in dark glass‑stoppered bottle.
Standard Sodium thiosulate titrant
Dilute the stock sodium thiosulfate solution to obtain 0.0125 N (100 ml of stock 0.125 N Na2S2O3 dilute to 1000 ml with distilled water gives 0.0125 N Na2S2O3) Standardize this diluted solution daily.

## Slide 56
Standardization
Pipette 10 ml 0.0125 N Potassium iodide into a conical flask containing about 100 ml distilled water. Add 2 ml of conc. H2SO4 followed by about 2 g of potassium iodide solid. Titrate immediately against sodium Thiosulfate (0.0125 N) using starch as indicator. Apply concentration correction in the calculation.

## Slide 57
PROCEDURE
Fill the bottle without turbulently exposing the sample to the air, and stopper it.
Rideal‑Stewart modification for examination of interference by ferrous ion.
This modification is used when the sample contains ferrous iron. Add 0.7 ml conc. H2SO4 followed by 1 ml potassium permanganate (0.61%) and 1 ml potassium Fluoride (40%) to the sample bottle, stopper and mix by inversion.
The amount of permanganate added should be just sufficient to obtain a violet tinge that persists for 5 min.
Remove the excess permanganate by adding 0.5 to 1.0 ml potassium oxalate (2%).
Mix well and let stand in the dark for 10 min. to facilitate the reaction.
Excess oxalate causes low results and hence add only an amount of oxalate that completely decolorizes the potassium permangante.

## Slide 58
After applying this modification usual method should be followed
Add 2 ml manganous sulfate followed by 2 ml alkali‑ iodide‑azide reagent, dipping the pipette little below the surface.
Stopper carefully to exclude air bubbles, and thoroughly mix the contents by inverting the bottle at least 15 times.
Allow the precipitate to settle to the lower one‑third of the bottle, repeat the mixing and allow the precipitate to settle completely leaving a clear supernant liquid.
Add 2 ml conc. H2SO4 immediately after removing the stopper. Restopper and mix by gentle inversion until all the precipitate dissolves, if it does not, allow standing for a few minutes and repeating the mixing.

## Slide 59
Distribute the iodine uniformly before taking a part of it titration.
Pipette 101.3 ml. of sample for titration (1.3 ml extra to account for 4 ml or the reagents, manganous sulfate and alkali‑iodide‑azide, added to 300 ml of sample) in a conical flask and immediately titrate the liberated iodine with the standard thiosulfate solution to a pale yellow straw colour.
Add 2 ml starch solution and continue the titration till the first disappearance of the blue colour.
Disregard subsequent recolouration due to the catalytic effect of nitrite or ferric salts.
It must be remembered that iodine is volatile and therefore, the titration must be carried out as expeditiously as possible and with the minimum of exposure to the air.
Notes: Expeditious: done with speed and efficiency: an expeditious investigation.

## Slide 60
Calculation :
Vol. of thiosulfate required for
Dissolved Oxygen mg/lit. = 10 X titration of 101.3 ml. sample
Vol. of thiosulphate required for 10 ml
of 0.0125 N Potassium iodate.
Notes: 1 ml of 0.025N Na2S2O3 = 0.2 mg of O2 D.O. in mg/l = (0.2 x 1000) x ml of thiosulphate
200

## Slide 61
Precision and Accuracy
The DO can be measured with a precision of about 50 g/l or 0.05 mg/l in surface and slightly polluted waters, expressed as standard deviation.
In the presence of appreciable interference this may be as high as 100 g/l or 0.1 mg/l.

## Slide 62
PRECAUTIONS
Determine DO at site, if not possible, at least fix at site and titrate in laboratory (add acid in the laboratory)
Do not use soap or synthetic detergents for washing the DO bottles/Normally bottles are kept clean by the acidic iodine solution of the Winkler procedure and require no further treatment except thorough rinsing with the tap water.
New bottles should be cleaner with 5 N sulfuric or hydrochloric acid and then rinsed thoroughly with the tap water.
Just before taking the sample rinse sample bottle with the sample.

## Slide 63
Bottle should be completely filled with the sample and remove bubbles entrapped into the bottle while taking sample by tapping the neck of the bottle with the stopper.
Fix the DO on the site by adding manganous sulfate and alkali‑iodide‑azide solution.The titration should be carried out as expediously as possible and with the minimum exposure to the air, so as to avoid any losses of iodine during titration.
Use BOD‑Sample discharger to avoid inconvenience caused in measuring 101.3 ml. This will save time as well as maintain uniformity in the analysis. Alternatively, use measuring cylinder.
Avoid errors due to carelessness in collecting the sample, prolonging the completion of the test or due to any interferences.

## Slide 64
Chemical Reactions
MnSO4 + 2 KOH --- Mn(OH)2 + K2 SO4 (white ppt)
2Mn(OH)2 + O2 --- 2 MnO(OH)2 (Brown ppt)
MnO(OH)2 + 2H2SO4 --- Mn(SO4)2 + 3H2O
Mn(SO4)2 + 2KI -- MnSO4 + K2SO4 + I2
2Na2S2O3.5H2O + I2 -- Na2S4O6 + 2NaI + 10H2O
2NaN3 + H2SO4 -- 2 N3H + Na2SO4
HNO2 + N3H -- N2 + N2O + H2O

## Slide 65
Manganous Sulphate Solution
Dissolve 480 g manganese sulphate (MnSO4.4H2O) in freshly boiled and cooled water, filter and make up to 1000 mL distilled. Check that the solution do not give blue colour by addition of acidified potassium iodide solution and starch.
Alkaline Iodide Solution
Dissolve 500 g of sodium hydroxide (or 700 g of potassium hydroxide) and 135 g of sodium iodide (or 150 g of potassium iodide) in freshly boiled and cooled water and dilute to 1 L.
Sulphuric Acid, (Concentrated)
Starch Indicator
Dissolve 2 g of starch and 0.2 g of salicylic acid as preservative, in 100 mL of hot distilled water.
Notes: REFERENCE
APHA (American Public Health Association), (1998): Standard method for examination of water and wastewater, 20th Edition, Washington, D.C., USA. p. 5.2 - 5.6.

## Slide 66
Sodium Thiosulphate Stock Solution
Dissolve approximately 25 g of sodium thiosulphate (Na2S2O3.5H2O) in boiled distilled water and make up to 1000 mL. Add 1 g of sodium hydroxide to preserve it. Store in a amber coloured bottle.
Standard Sodium Thiosulphate Solution
Dissolve 250 mL of stock solution in boiled distilled water and make up to 1 L and standardize to 0.0125 N sodium thiosulphate against known standard potassium iodide solution before use.

## Slide 67: PART-II: ANALYSIS OF FOOD SAMPLE
Many of the methods in use today for the analysis of foods are procedures based on a system introduced initially about 100 years ago by Germans for the analysis of animal feedstuffs and described as the Proximate Analysis of Foods.
This scheme of analysis involves the estimation of the main components of a food using procedures that allow a reasonably rapid and acceptable measurement of various food fractions without the need for sophisticated equipment or chemicals.

## Slide 68: ANALYSIS OF FOOD SAMPLE (conti..)
Many of the basic principles of the analytical procedures remain fundamentally the same as the original system, major advances have taken place , particularly in the use of automated equipment and of sophisticated analytical instruments enabling many of the analyses to be performed more rapidly and with a greater degree of precision.
The Proximate Analysis of Foods involves the determination of the following constituents:
Loss on drying iv) Ether extract vii) available carbohydrate
Mineral elements v) protein viii) unavailable carbohydrate
Fat vi) carbohydrate ix) fiber x) Non-starch polysaccharides
xi) Dietary fiber Xii) Neutral detergent fiber

## Slide 69: ANALYSIS OF FOOD SAMPLE (conti..)
However, the move from traditional, classical or wet chemistry techniques to modern instrumentation methods has not necessarily meant that the traditional methods have been discontinued since , in many instances, instrumental methods require an initial calibration of the instrument against results produced by the traditional methods.

## Slide 70: ANALYSIS OF FOOD SAMPLE (conti..)
Increased awareness and knowledge about nutritional and functional properties of various food constituents has resulted in a greater body of information being required for particular foods
Example : The degree of saturation constituent fats, the levels of individual minerals and vitamins and the amount of minor constituents such as trace elements.
Consequently, the modern analysis of a food generally requires many more estimations to be performed that in the original scheme of analysis and this, in turn, involve the use of a wide range of different techniques and principle.

## Slide 71: Techniques used in food analysis
Procedures involving traditional wet chemistry techniques have played an important role in food analysis since the original scheme of proximate analysis was first postulated
Whilst the use of such methods may have decreased in popularity in recent times, they still have a particularly important to play and are still commonly used on the basis of cost, simplicity of operation and requirement for calibration of modern analytical instruments

## Slide 72
DISADVANTAGES: lack of sensitivity and specificity for the analysis of certain constituents.
METHODS: titrimetric analysis, gravimetric procedures, solvent extraction, refractometry, polarimetry etc
Modern methods of analysis allows the food chemist to choose between a wide range of techniques including:

## Slide 73
SPECTROSCOPIC METHODS
Colorimetric and UV/ Visible
Infrared Spectrophotometry
Flame photometry
Atomic Absorption Spectrophotometry
NMR Spectroscopy
CHROMATOGRAPHY
Paper and thin-layer chromatography
Gas chromatography
High performance Liquid chromatography

## Slide 74
EXPERIMENTAL PROCEDURES FOR THE ESTIMATION OF MAJOR FOOD CONSTITUENTS
Many of the procedures described in this manual involve the use of chemicals, which if handled in an inappropriate manner, may pose hazards to the operator or to other personnel. Particular case should thus be taken in all laboratory procedures.
SAMPLING
Prior to each analysis, a representative sample of the food and should follow the guidelines indicated below.
DRY FOODS
Normally the food should be passed through a grinder and then mixed in mortar
MOIST FOODS
Foods such as meat and fish products and vegetables should be treated as for dry foods and the process repeated at least once before transferring the mixture to closed container and storing it under refrigeration.
WET FOODS
Foods such as pickles sauces and canned products are often best treated in high speed blender. Care must be taken to avoid fat separation with emulsions such as salad cream and cream soups

## Slide 75: EXPERIMENT 1: DETERMINATION OF MOISTURE AND TOTAL SOLIDS PRESENT IN A GIVEN FOOD
Principle: A known weight of food sample is dried to constant weight in an oven and the loss of weight is equated to the moisture content of the food
Apparatus: Crucibles, drying oven at 101 – 105°c; glass rods, desiccator, balance, steam bath, sand

## Slide 76
PROCEDURE
Specific procedures are recommended for individual food products. The following procedures suitable for the range of food types indicated.
COMPOSITE FOODSTUFFS , FRUIT AND VEGETABLES:
Dry a coded, clean crucible (or other suitable container) either over a Bunsen burner for few minutes or by placing in an oven for about 30 minutes, cool in desiccator and weigh.
Weigh the crucible along with a small (clean and dry) mixing rod.
You may add up to 1 g of fine sand to assist moisture removal
Weight a accurately 4 - 6 g of the food into the crucible and mix with a small amount water, using the glass rod to aid with the mixing .
Record the weight of crucible plus rod plus food.

## Slide 77
For every wet samples, place on a steam bath until the excess water has evaporated
Dry in an oven at 101 – 105 °C to constant weight, allowing at least 2 hours (preferably overnight).
Remove and cool in a desiccator.
Record the weight of the plus contents after drying and calculate the moisture and total solids content of the food by assuming that the loss in weight of the sample on drying is due to the loss of moisture only.
Where overnight drying has not been undertaken, the drying process should be repeated for further 30 minute period until successive weightings differ by less than 0.1 % of the food sample.

## Slide 78
DAIRY AND MEAT PRODUCTS
The procedure is similar to above, but uses sand to aid the drying process.
Place about 20 g of sand into a coded, clean crucible (or other suitable container) and dry by placing in an oven for about 30 minutes, cool in a desiccator and weigh along with a small glass rod.
Record the weight of crucible plus rod plus food.
Weight accurately 4 – 6 g of the food into the crucible and mix with a small amount of water, using the glass rod to aid with the mixing.
Record the weight of crucible plus sand plus food.
For very wet samples, e.g. milk, place on steam bath until the excess water has evaporated.
Dry in an oven at 101 – 105°C to constant weight, allowing at least 2 hours (preferably overnight).

## Slide 79
Remove and cool in a desiccator. Record the weight of the crucible plus contents after drying and calculate the moisture and total solids content of the food by assuming that the loss in weight of the sample on drying is due to the loss of moisture only.
Where overnight drying has not been undertaken, the drying process should be repeated for further 30 minutes period until successive weightings differ by less than 0.1% of the original mass of the food sample.
In your report do the following calculations:
%Moisture = (W2 - W3) × 100
( W2 - W1)
Where: W1, the initial weight of empty crucible + rod (+ sand);
W2, the weight of crucible + food + rod (+sand) before drying
W3, the final weight of crucible + food+ rod (+sand) and
% Total solids = 100 - %Moisture

## Slide 80
Experiment 2: Determination of the ash content of a given food sample
Principle
The total mineral content of a food may be estimated as the ash content, which is the inorganic residue remaining after the organic matter has been burnt away.
Apparatus: Crucibles, hotplate, desiccator, muffle furnace at 550°C water bath or dry oven
Procedure
Weigh accurately 4 – 6 g of the food into a previously ignited, cooled and weighted crucible.
For high moisture foods or liquid samples, evaporate to dryness or small volume on a water bath or in an oven at 100°C.
For flour, milled rice and other milled cereals, add a few drops of glycerol and mix.
Heat gently over a Bunsen burner until the food is charred. Transfer the crucible to a muffle furnace at about 550°C and leave until a white or light grey ash results.
If the residue is black in color, moisten with a small amount of water, to dissolve salts, dry in an oven and repeat the ashing process.
Cool in a desiccator and reweigh.

## Slide 81
Calculation:
Calculate the total ash as a percentage of the original sample given that
%of ash = weight of ash × 100
weight of original food
= (W3 – W1) × 100
(W2 – W1)
Where W1, the weight of empty crucible;
W2, the weight of crucible + food before drying
W3, the final weight of crucible + ash
Note: Retain the ash where the determination of individual minerals is to be performed.

## Slide 82
Preparation of ash solution
To the crucible add 5 mL of concentrated hydrochloric acid and boil the mixture for 5 minutes on a hot plate in a fume cupboard, adding acid as necessary to maintain the volume.
Transfer to a beaker and wash the crucible into the beaker with distilled water. Adjust the volume to about 40 mL and boil for 10 minutes over a Bunsen burner .
Cool and filter in a 100 mL volumetric flask and rinse the beaker with distilled water into volumetric flask. Cool and make up to the volume mark (100 mL). Use this ash solution for determination of individual minerals.

## Slide 83
Experiment 3: Determination of the calcium in foods by permanganate titration
Principle:
Calcium is precipitated at about pH 4 as the oxalate (any phosphate present being removed with acetic acid), and the oxalate is then dissolved in sulfuric acid, liberating oxalic acid, which is titrated with standard potassium permanganate solution.
Calcium is precipitated by ammonium oxalate
CaCl2 + (NH4)2C2O4  2NH4Cl + CaC2O4
Oxalic acid is liberated by the action of sulfuric acid on calcium oxalate
CaC2O4 + H2SO4  CaSO4 + H2C2O4
The free oxalic acid is then titrated with potassium permanganate
5H2C2O4 + 2KMnO4 + 3H2SO4  K2SO4 + MnSO4 + 8H2O + 10CO2
Apparatus: Burette, 50 mL pipette, Filter paper

## Slide 84
Reagents: 0.01 M potassium permanganate, Dilute ammonium hydroxide solution, Dilute acetic acid, Solid ammonium oxalate, Dilute sulfuric acid and Calcium chloride solution
PROCEDURE:
Prepare an ash solution of the food as described previously
Neutralize 50 mL of this ash solution in a 250 mL beaker with dilute ammonium hydroxide until it is just alkaline to litmus and then just acidify with dilute acetic acid. Bring to boil (on water bath or hot plate), add an excess of ammonium oxalate (0.8 g), boil vigorously for 1 min and then gently for 30 minutes. Pour the supernatant liquid through a 12.5 cm Whatman No. 1 ( or similar) filter paper in a funnel and wash the precipitate twice, with hot water, by decantation through the same filter.
Finally transfer the precipitate from the beaker to the paper and wash the residue to the filter paper a number of time with small quantities of distilled water. The washing should be continued until the filtrate is free from oxalate. This is shown by collecting a few drops of the filtrate, at intervals, in a test tube and adding calcium chloride solution.
A white precipitate indicates the presence of oxalate.

## Slide 85
Discard the filtrate and washing, transfer the filter paper carrying the precipitate to the beaker used for the precipitation and add 60 mL of warm bench dilute sulphuric acid.
Stir the contents of the beaker, macerating the filter paper. Warm to 70°C and titrate with 0.01M potassium permanganate solution to a persistent pink color.
Calculation:
Calculate the percentage of calcium in the original food given that:
% Calcium in food = T× 0.1/W
Where: T = titer of 0.01 M potassium permanganate, and
W = Weight of original food ashed

## Slide 86
Experiment 4: Determination of phosphorus in foods by the vanadate colorimetric method
PRINCIPLE: Phosphorus may be determined as phosphate by the vanadium phosphomolybdate (vanadate) colorimetric method in which the phosphorus present as the orthophosphate reacts with a vanate-molybdate reagent to produce a yellow-orange complex, the absorbance of which is measured at 420 nm.
APPARATUS:100 mL volumetric flask; spectrophotometer at 420 nm or colorimeter with blue filter Pipettes, beakers
REAGENT:(i) Vanadate-molybdate reagent: Dissolve 20g ammonium molybdate in 400 mL water at about 50°C and cool. Dissolve 1 g ammonium vanadate in 300 mL of boiling distilled water, cool and add 140 mL concentrated nitric acid gradually with string. Add the molybdate solution gradually, with stirring, to the acid vanadate solution and dilute to 1 liter with distilled water

## Slide 87
(ii) Standard phosphate solution: dissolve 4.39 g of potassium dihydrogen phosphate per liter of distilled water. Dilute 25 mL to 250 mL with distilled water to give a solution containing 0.1 mg per mL.
PROCEDURE:
Calibration to a series of 100 mL volumetric flasks add 0, 2.5, 5.0, 7.5 and 10.00 mL of the standard phosphate solution and dilute each with about 30 mL distilled water. Add 25 mL of the vanadate-molybdate reagent to each dilute to the mark and mix well by inversion. Allow to stand for 10 minutes and then measure the absorbance of each solution using the 0 mL solution to zero the instrument.
Analysis of food sample solution: Prepare an ash solution of the food as described previously. Pipette 2.00 mL of the ash solution into a 100 mL volumetric flask. Then proceed as for the standard solutions above i.e. adding 25 mL of the vanadate – molybdate reagent, diluting to the mark, mixing and measuring the absorbance after allowing to stand for 10 minutes.(If the colr of the solution obtained is greater than that of the highest standard, repeat the procedure using a smaller volume than 2.0 mL. If the color is much paler than that of the lowest standard repeat using a larger volume than 2.0 mL).

## Slide 88
Prepare a table and plot a calibration graph of absorbance against mg P per 100 mL
If concentration of diluted ash solution (from graph) = A mg P per 100mL, weight of original food ashed = Wg,
volume of ash solution diluted to 100 mL = v mL, then
%P content of original food = (A×10)/ (W × V)
Table. 1. Concentrations for calibration graph for vanadate estimation of Phosphorus
S.No | mL standard phosphate solution per 100 mL | mg P per 100 mL | Absorbance

## Slide 89
Experiment 5: Micronutrient Analysis of food samples by wet Digestion
Full recovery of micronutrients cations (Zn, Fe, Mn, Cu) in high-silica containing plant tissues (like wheat, barley, rice, sugarcane, etc.) is not possible by dry ashing procedure. Therefore, this kind of plant materials should be wet-digested using HNO3-HClO4. Many other elements (like P, K, Ca, Mg, Na) can also determined in the same digest.
APPARATUS: Block- digester, Vortex tube stirrer, Atomic absorption spectrophotometer, Flamephotometer
REAGENT: Nitric Acid-per chloric Acid (HNO3-HClO4), 2:1 ratio (To 1 L concentrated nitric acid add 500 mL concentrated per chloric acid)

## Slide 90
PROCEDURE:
A. Digestion
1. Weight 1 g of the corn or wheat flour (or any other dry food sample supplied by TA), and then transfer quantitatively into a 100-mL Pyrex digestion tube.
2. Add 10 mL 2:1 nitric-per chloric acid mixture, and allow to stand overnight or until the vigorous reaction phase is over.
3. Connect to a condenser and place the tubes in a cold block-digester, and then raise temperature to about 150°C for 1 hour and slightly increase the temp. Up to about 200°C.
4. Note time, when dense white fumes of perchloric acid appear in the tubes, and continue digestion for 30 minutes more
5. Lift the tubes rack out of the block digester, allow to cool a few minute, and add a few drops dilled water carefully through a funnel
6. After vapors condense, add distilled water in small increments for washing down walls of tubes
7. Transfer to 100 mL volumetric flask by passing through a filter paper and bring to volume with distilled water.
8. Each batch of samples for digestion should contain at one blank (no plant material)

## Slide 91
B. Measurement
Analyze Zn, Fe, Cu, Ca and Mg in the aliquots by Atomic Absorption Spectrophometry.
Determine K and Na by Flame Photophotometry or Atomic Emission Spectrophotometer
C. In your report include:
Calculation of the concentrations of Zn, Fe, Cu, Ca, Mg, K and Na in units of mg/g of sample as follows;
= (ppm in sample-blank) × volume of solution (L)
Weight of dry sample (g)

## Slide 92: Part III: SOIL SAMPLE ANALYSIS
Nature of soil
What is Soil? Soil may be defined as the naturally deposited unconsolidated material which covers the earth’s surface whose chemical, physical and biological properties are capable of supporting plant growth.
Soil is a product of natural decomposition forces acting upon native rocks, vegetation and animal matter over an extremely long period of time, in some cases literally thousands of years.

## Slide 93: Experiment one: Determination of Organic Carbon of Soil Sample
Principle: The importance of organic carbon estimation lays in the fact that it gives an indication of the organic matter content of the soil