## Slide 1: CHAPTER TWO
Main Petrochemicals

## Slide 2: Main Petrochemicals
What are Petrochemicals?
 How Petrochemicals are obtained?
 Why we need to study Petrochemicals?
 What are the applications of Petrochemicals?

## Slide 3: 2.1. Introduction to petrochemicals
What are Petrochemicals?
A petrochemical is any chemical (as distinct from fuels and petroleum products) manufactured from petroleum and used for a variety of commercial purposes.
They are non-fuel chemical compounds derived from petroleum.
These chemicals include a large no of organic compounds (aliphatic & aromatic) of various functional groups.

## Slide 4: 2.1. Introduction to Petrochemicals
Primary petrochemicals include:
olefins (ethylene, propene, and butadiene)
aromatics (benzene, toluene, & xylene), &
 methanol.
Thus, petrochemical feed-stocks can be classified into different groups: olefins, aromatics, and methanol;
a 4th group includes inorganic compounds & synthesis gas.

## Slide 5: Introduction to petrochemicals
The common products made from petrochemicals include:
 plastics, soaps, detergents, solvents, adhesives
 paints, drugs, fertilizer,
 pesticides, insecticides, explosives,
 synthetic fibers, synthetic rubber,
 flooring, and insulating materials.

## Slide 6: 2.2. Chemical Conversions for Manufacture of Petrochemicals
The conversion of refinery feedstock into final products involves three main stages.
1st stage is the manufacture of the base chemicals or the building blocks .
e.g. ethylene, propylene, benzene.
Then they are converted into intermediate products
e.g. ethanol, ethylene glycol, propylene glycol, styrene, etc.
3rd stage, these intermediate are then further converted into products that are used directly by industry to produce finished consumers products.
e.g. polyethylene, polypropylene, polystyrene, polyvinylchloride

## Slide 7: contd
The base chemicals can be broadly classified into two groups: olefins and aromatics.
Olefins are characterized by chains of C atoms as their backbone while aromatics contain a ring of C atoms at the core of the molecule.
In an olefin plant, the long chained C molecules are cracked into smaller chains, such as C2 (ethylene), C3 (propylene) & C4 (butadienes).
The two cracking methods used are thermal cracking (high temp.) & catalytic cracking, both of which are highly energy intensive.

## Slide 8: 2.3. Petrochemicals from Methanol, Ethylene, Propylene, Butylenes & BTX
How Petrochemicals can be manufactured from Methanol, Ethylene, Propylene, Butylenes and BTX?
The two petrochemical classes are olefins including ethylene and propylene, & aromatics including benzene, toluene and xylene isomers(BTX).
Oil refineries produce olefins & aromatics by fluid catalytic cracking of petroleum fractions.
Chemical plants produce olefins by steam cracking of natural gas liquids like ethane and propane.

## Slide 9: Petrochemicals from Methanol, Ethylene, Propylene, Butylenes & BTX
Aromatics are produced by catalytic reforming of naphtha.
Olefins and aromatics are the building blocks for a wide range of materials such as solvents, detergents, & adhesives.
Olefins are the basis for polymers and oligomers used in plastics, resins, fibers, elastomers, lubricants, and gels.
2.3.1 Primary Petrochemicals
They are divided into three groups depending on their chemical structure:
Olefins include ethylene, propylene, and butadiene.
Ethylene & propylene are important sources of industrial chemicals & used in manufacturing of plastic products similarly, butadiene is used in making synthetic rubber.

## Slide 10: contd
Aromatics include benzene, toluene, & xylenes(BTX).
Benzene is a raw material for dyes & synthetic detergents.
Manufacturers use xylenes to produce plastics & synthetic fibers.
Synthesis gas is a mixture of CO & H2 used to make NH3 & methanol.
NH3 is used to make the fertilizer urea & methanol is used as a solvent & chemical intermediate.

## Slide 11: contd
.

## Slide 12: contd
Benzene

## Slide 13: 2.4 Manufacture of Acetylene, Ethylene oxide, Acrylonitrile, Dimethylterephthalate
2.4.1 Manufacture of Acetylene (C2H2)
C2H2 is manufactured from CaC2 & H2O.
Besides, there are other methods that can be used for the preparation of C2H2.
C2H2 is a colorless, combustible gas with a distinctive odor.

## Slide 14: contd
These processes use high temp. (thermal cracking process) to convert the raw materials into a wide variety of gases, including H, CO, CO2, C2H2 and others.
The chemical reaction for converting CH4 into C2H2 & H may be written:

## Slide 15: Uses of Acetylene
The most common use of C2H2 is as a raw material for the production of various organic chemicals including 1,4-butanediol, which is widely used in the preparation of polyurethane and polyester plastics.
The second most common use is as the fuel component in oxy-acetylene welding and metal cutting.
Some commercially useful C2H2 compounds include C2H2 black, which is used in certain dry-cell batteries, & acetylenic alcohols, which are used in the synthesis of vitamins.

## Slide 16: 2.4.2 Manufacture of Ethylene oxide (C2H4O)
C2H4O is a flammable, colorless gas.
C2H4O is found in the production of solvents, antifreeze, textiles, detergents, adhesives, polyurethane foam, and pharmaceuticals.
It is also useful in fumigants, sterilants for spices & cosmetics, as well as during hospital sterilization of surgical equipment.
In industry C2H4O is produced while C2H2 & oxygen reacting on a silver catalyst at 200–300°C & pressures used are in the region of 1-2MPa.

## Slide 17: Uses of ethylene oxide
The chemical compound C2H4O is an important industrial chemical used as an intermediate in the production of ethylene glycol, other chemicals, & sterile for the manufacturing of rubber, paint, leather processing, industrial surfactants, paper, textile, metal processing, latex & waxes, household surfactants, detergents, pharmaceutical raw materials, dyeing & finishing, agrochemicals, cosmetics raw material.

## Slide 18: 2.4.3 Manufacture of Acrylonitrile (C3H3N)
Acrylonitrile, vinyl cyanide, CH2=CHC≡N, is a colorless liquid with a slightly pungent odor.
It was first prepared in 1893 by a French Chemist, Ch. Moreau, by dehydration of ethylene cyanohydrin with phosphorus pentoxide.
It is an important monomer for the manufacture of useful plastics.
Most industrial acrylonitrile is produced by catalytic ammoxidation of propylene by the Sohio process in the presence of a metal-oxide catalyst.

## Slide 19: 2.4.4 Manufacture of Dimethyl terephthalate (DMT)
The most important commercial route to ester & acid manufacture is the liquid-phase oxidation of p-xylene.
The crude esters are separated into their components in a system of columns under vacuum.
The DMT is further purified by recrystallizing twice from methanol or xylene, melted, and converted into readily manageable flakes with a drum flaker.
DMT is used in the manufacture of polyester fibre, yarn & film and also certain polyester resins.