## Slide 1: Fundamentals of Analytical chemistry (221)
CHAPTER-3
Manufacture of Inorganic Acids (Hydrochloric, Hydrofluoric& Sulfuric acids)

## Slide 2: Cont’.....
Introduction
Hydrochloric, Hydrofluoric & Sulfuric acids are some of the important inorganic acids that are widely used in industry and laboratory.
In this chapter we are going to discuss about :
  the use of,
  method of preparation and
  properties of Hydrochloric, Hydrofluoric & Sulfuric acids.
Methods of manufacture of hydrochloric acid and its uses
Hydrochloric acid is a monoprotic acid.
In aqueous hydrochloric acid, the H+ joins a water molecule to form a hydronium ion, H3O+. Which means it can dissociate
HCl + H2O → H3O+ + Cl-

## Slide 3: Cont’.....
The other ion formed is Cl-, the chloride ion.
Hydrochloric acid can therefore be used to prepare salts called chlorides, such as NaCl.
HCl is a strong acid; it is essentially completely dissociated in water. HCl is the preferred acid in titration for determining the amount of bases.
Concentrated hydrochloric acid dissolves many metals and forms oxidized metal chlorides and hydrogen gas,

## Slide 4: Preparation of HCl
The following methods are used for the preparation of HCl and each method involves two stages.
  Production of HCl gas
  Absorption of HCl in water
Methods of production
Chlorination of aliphatic and aromatic hydrocarbons,
HCl is the by-product
CH4 + Cl2 + hv → CH3Cl + HCl
C6H6 + Cl2 + hv → C6H5Cl + HCl
2. Sulphate method; this method is based on the reaction of sodium chloride with sulphuric acid.

## Slide 5: Cont’.....
    NaCl + H2SO4 → HCl + NaHSO4
    NaCl + NaHSO4→ HCl + Na2SO4
The net reaction is: 2NaCl + H2SO4 → Na2SO4 + 2HCl
This reaction is carried out at 500-5500C. The yield is 39-40% by weight.
3. Direct synthesis
Hydrogen burns in chlorine exothermically.
H2 + Cl2 → 2HCl
Industrially the above reaction is carried out by burning H2 in Cl2 at 23000C-24000C.
The gas leaving the furnace contains 80-90% of HCl

## Slide 6: Cont’.....

## Slide 7: Cont’.....
Uses of HCl

## Slide 8: Cont’.....
One of the most important applications of HCl is in the pickling of steel, to remove rust or iron oxide scale from iron or steel before subsequent processing, such as extrusion, rolling, galvanizing, and other techniques.
Technical quality of HCl at typically 18% concentration is the most commonly used pickling agent for the pickling of carbon steel grades.
Fe2O3 + Fe + 6HCl→ 3FeCl2 + 3 H2O
Another major use of HCl is in the production of organic compounds, such as vinyl chloride and dichloroethane for PVC.
2CH2=CH2 + 4HCl +O2→2ClCH2CH2Cl + 2H2O
(dichloromethane by oxychlorination)
Wood + HCl + heat → Activated carbon
Numerous products can be produced with hydrochloric acid in normal acid-base reactions, resulting in inorganic compounds.

## Slide 9: Cont’.....
Industrial manufacture of hydrofluoric acid and its uses
Hydrofluoric acid (HF) is a solution of hydrogen fluoride in water.
While it is extremely corrosive and difficult to handle, in the technical sense, it is a weak acid.
Hydrogen fluoride, often in the aqueous form as hydrofluoric acid, is a valued source of fluorine.
diverse polymers such as polytetrafluoroethylene(Teflon), and
most other synthetic materials that contain fluorine.
Hydrofluoric acid is the best known to the public for its ability to dissolve glass by reacting with SiO2
The major component of most glass, to form silicon tetra fluoride gas and hexafluoro silicic acid.

## Slide 10: Cont’.....
Because of its high reactivity toward glass, hydrofluoric acid must be stored (in small quantities) in polyethylene or Teflon containers.
It is also unique in its ability to dissolve many metal and semimetal oxides.
Due to its low degree of ionization in dilute solution, hydrofluoric acid is the only hydrohalic acid that is not considered as strong acid.
Industrial manufacture of hydrofluoric acid
In industry, hydrofluoric acid is produced by treatment of the mineral fluorite (CaF2) with concentrated sulfuric acid.
When combined at 250oC, these two substances react to produce hydrogen fluoride and calcium sulfate according to the following chemical equation:

## Slide 11: Cont’.....
CaF2 + H2SO4 → 2 HF + CaSO4
Most HF is produced as a by-product of the production of phosphoric acid, which is derived from the mineral apatite(phosphate mineral) with the formula Ca5(PO4)3F).
Use of HF
Hydrofluoric acid (HF) has various uses.
It is used as a catalyst in oil refining
It is used in the production of organofluorine compounds e.g., many organofluorine compounds are prepared using HF as the fluorine source, including Teflon[(C2F4)n], fluoropolymers, fluorocarbons, and refrigerants such as Freon(CCl2F2).

## Slide 12: Cont’.....
It is used for production of fluorides.
Many high volume inorganic fluoride compounds are prepared from hydrofluoric acid.
For example: cryolite(Na3AlF6) , AlF3 and etc
It removes oxide impurities from stainless steel, a process called pickling (of preserving food), and silicon wafers in the semiconductor industry.

## Slide 13: Cont’.....
Chamber process and contact process of manufacture of sulphuric acid & its handling
Sulfuric (or sulphuric) acid, H2SO4 is a strong mineral acid.
It is soluble in water at all concentrations.
it is a clear, colorless, odorless, viscous liquid that is very corrosive.
Sulfuric acid is very stable oxyacid's of sulfur.
It is often called king of chemicals, since it is one of the most useful chemicals which is extensively used in industries.
Sulfuric acid has many applications, and is one of the top products of the chemical industry.
Principal uses include ore processing, fertilizer manufacturing, oil refining, wastewater processing, and synthesis.

## Slide 14
Manufacturing of sulfuric acids
There are two general methods of manufacturing of sulfuric acid.
These are Lead chamber process and contact process.
i) Manufacture of H2SO4 by Lead Chamber process
Lead chamber process: In the original lead chamber process, sulfur and potassium nitrate are ignited in a room lined with lead foil
Potassium nitrate, or saltpeter is an oxidizing agent oxidizes the sulfur to sulfur trioxide according to the reaction:
6KNO3(s) + 7S(s) →3K2S(s) + 6NO (g) +4SO3 (g)
When the sulfur trioxide reacted with the water, sulfuric acid was produced:
SO3 (g) + H2O (l) →H2SO4 (aq)
Cont’.....

## Slide 15: Cont’.....
This process is a batch process and can be formed in the consumption of potassium nitrate.
ii) Manufacture of H2SO4 by double adsorption contact process
Sulfuric acid is produced from sulfur, oxygen and water via the contact process.
In the first step, sulfur is burned to produce sulfur dioxide
S(s) + O2(g) → SO2(g)
This is then oxidized to sulfur trioxide using oxygen in the presence of a vanadium (V) oxide catalyst.
(2) 2 SO2 + O2(g) → 2 SO3(g) (in presence of V2O5)

## Slide 16: Cont’.....
For example: In our country, in Awash Melkasa H2SO4 ,there are four converters or beds that are used for conversion of SO2 to SO3 by using V2O5 catalyst
In 1st bed, 63% SO2 is changed to SO3, in second bed 87% SO2 is changed to SO3, in third bed 96% SO2 is changed to SO3 and finally in the fourth bed 98.5% SO2 is changed to SO3.
Finally, the sulfur trioxide is treated with water (usually as 97-98% H2SO4 containing 2-3% water) to produce 98-99% sulfuric acid.
(3) SO3(g) + H2O(l) → H2SO4(l)
Note that directly dissolving SO3 in water is impractical due to the highly exothermic nature of the reaction, forming a corrosive mist instead of a liquid.

## Slide 17: Cont’.....
Alternatively, SO3 can be absorbed into H2SO4 to produce oleum (H2S2O7), which may then be mixed with water to form sulfuric acid.
(3) H2SO4(l) + SO3 → H2S2O7(l)
Oleum is reacted with water to form concentrated H2SO4.
(4) H2S2O7(l) + H2O(l) → 2 H2SO4(l)
Today, nearly all of the world’s sulfuric acid is produced by using this method.
Physical properties of H2SO4
Forms of sulfuric acid
Although nearly 100% sulfuric acid can be made, this loses SO3 at the boiling point to produce 98.3% acid.

## Slide 18: Cont’.....
The 98% grade is more stable in storage, and is the usual form of what is described as concentrated sulfuric acid.
Other concentrations are used for different purposes.
Some common concentrations are:
  10%, dilute sulfuric acid for laboratory use,
  33.5%, battery acid (used in lead-acid batteries),
  62.18%, chamber or fertilizer acid,
  77.67%, tower or Glover acid,
  98%, concentrated acid

## Slide 19: Cont’.....
Chemical properties H2SO4
Reaction with water
The hydration reaction of sulfuric acid is highly exothermic.
If water is added to the concentrated sulfuric acid, it can boil and spit dangerously.
One should always add the acid to the water rather than the water to the acid.
This can be remembered through such as: Add Acid", or "Drop acid, not water", or "Acid to water, " or "Put the king into the water, not the water into the king" .

## Slide 20: Cont’.....
The necessity for this safety precaution is due to the relative densities of these two liquids.
Water is less dense than sulfuric acid, meaning water will tend to float on top of this acid.
Environmental aspects
Sulfuric acid is a constituent of acid rain, which is formed by atmospheric oxidation of sulfur dioxide in the presence of water - i.e. oxidation of sulfurous acid.
Sulfur dioxide is the main by product produced when sulfur-containing fuels such as coal or oil are burned.

## Slide 21: Cont’.....
Sulfuric acid is a very important commodity chemical, and indeed, a nation's sulfuric acid production is a good indicator of its industrial strength.
The major use (60% of total production worldwide) for sulfuric acid is in the "wet method" for the production of phosphoric acid, used for manufacture of phosphate fertilizers as well as trisodium phosphate for detergents.
The overall process can be represented as:
Ca5F(PO4)3 + 5 H2SO4 + 10 H2O → 5 CaSO4•2 H2O + HF + 3 H3PO4

## Slide 22: Cont’.....
Sulfuric acid is used in large quantities by the iron and steel making industry to remove oxidation, rust and scale from rolled sheet and billets prior to sale to the automobile and white-goods industry.
Another important use for sulfuric acid is for the manufacture of aluminum sulfate, also known as paper maker's alum.
This can react with small amounts of soap on paper pulp fibers to give gelatinous aluminum carboxylates, which help to coagulate the pulp fibers into a hard paper surface.
It is also used for making aluminum hydroxide, which is used at water treatment plants to filter out impurities, as well as to improve the taste of the water.

## Slide 23: Cont’.....
Aluminum sulfate is made by reacting bauxite with sulfuric acid:
Al2O3 + 3 H2SO4 → Al2 (SO4)3 + 3 H2O
Sulfuric acid is used for a variety of other purposes in the chemical industry.
For example, it is the usual acid catalyst for the conversion of cyclohexanoneoxime to caprolactam, used for making nylon.
Sulfuric acid is also important in the manufacture of dyestuffs solutions and is the "acid" in lead-acid (car) batteries.
Sulfuric acid is also used as a general dehydrating agent in its concentrated form.
Therefore, safety is needed in order to minimize Laboratory and Industrial hazardous.